## Slide 1: The Airborne Internet

## Slide 2: Outline
What is the Airborne Internet.
How AI works.
Subscriber units.
Difference between Satellite and AI.
One Type of Airplanes.
Conclusion.

## Slide 3: What is Airborne Internet
Some internet service:
1- cable TV
2- DSL
What is (AI)?
It is an internet broadband which Provide high-speed wireless internet connection by placing aircraft in fixed path over hundreds of cities

## Slide 4: What is Airborne Internet
(AI) deliver high-speed internet :
Around 25Mb/s for business users
And around 5 Mb/s for home users
(AI) uses a network called High Altitude Long Operation (HALO)
This network is used by U.S. army.

## Slide 5: How AI Work
The aircraft work as hub
HALO work as wireless network with star topology
(ISP) Internet Service Provider send the data through a gateway to the hub in the aircraft

## Slide 6: How AI Work
AI divide the area into different cells.
(mobile cells)
each spot beam serves a single "cell" on the ground in a frequency-division multiplex fashion with 5-to-1
four sub-bands for subscriber units
(A,B,C and D)
The fifth sub-band for the gateway
(E)

## Slide 7: How AI Work
To provide the service for 24 hours, three aircraft will be used. Each one for 8 hours.

## Slide 8: How AI Work
This service can cover cities
area around 75 mile in diameter
The aircraft will fly at altitude 51,000 ft
(15,500 m)
It use high-frequency.
between 28-38 GHz

## Slide 9: Subscriber units
The user terminal consists of three main parts:
1- The radio frequency unit (RU)
a) MMW Antenna
b) MMW Transceiver
c) An antenna tracking unit
An antenna tracking unit uses a pilot tone transmitted from the HALO aircraft to point its antenna at the airplane
2- The Network Interface Unit (NIU)
3- the application terminals such as PCs, telephones, video servers, etc.

## Slide 10: Subscriber units

## Slide 11: Difference between Satellite and AI
AI does not need frequency bands license
Can service hundred-thousand of broadband subscribers
Single link delays range from ~60 msec under the airplane to ~200 msec at the edge of the signal

## Slide 12: Difference between Satellite and AI
 | AI service | Satellite
Time delay | Small delay | Big delay
Frequency | 28-38 GHz | 4-6 GHz 9-13 GHz
Power | Low Power | High Power
Cost | Low Cost | High Cost

## Slide 13: the Proteus airplane
The Proteus was developed by NASA
It is designed with long wings and low wing loading
It can fly in high-altitude
18-foot dish underneath the plane is responsible for reflecting high-speed data signals from a ground station to users.

## Slide 14: Conclusion
The airborne internet provide high-speed internet.
AI has many advantage than satellite communication.
This new service will be useful for who live in small village

## Slide 15: Source
http://www.isoc.org/inet99/proceedings/4d/4d_3.htm#s15
http://computer.howstuffworks.com/airborne-internet.htm
IEEE Communications Magazine • June 2000
page 142-148
MWCON'98 Proceedings page 9-14

## Slide 16: Question
1- What is (AI) ?
It is an internet broadband by aircraft.
2- the aircraft works as
A- hub B- server C- ISP
3- which type of topology (HALO) use:
A- mesh topology B- star topology C- Ring topology
4- the frequency of (AI) is:
A- 20-30 MHz B- 28-38 KHz C- 28-38 GHz
5- the device which is used the pilot tone to direct the antenna is:
A- MMW Antenna B- MMW transceiver C- An antenna tracking unit